## Slide 1: Ascend MultiVoice Voice-over-IP Networks
“From Dial-Tone to Data-Tone”
Jose R. Garcia
Product Manager

## Slide 2: Overview
Key Trends in the Industry
MultiVoice Voice-over-IP Product Offering for the MAX
Network Integration
MultiVoice for MAX Release 1.0 Specifics
Applications
Summary

## Slide 3: Data Now Drives Networking Architectures
“New Public Data Network”
TDM Based
Voice Network
Time
Bits/Sec
Data now drives the network rather than Voice
Envision a network that is packet/cell-focused leveraging high-speed switching with fiber in the Core
Network Architectures are Voice Centric

## Slide 4: Technology Changes Pose a Threat to Incumbents, Moreover...
Source: The Net Effect

## Slide 5: It Presents a Considerable Opportunity for Growth
Source 1 & 2: IDC
Source 3: InfroTEST International
Source 4: Probe Research
60 million PC users will be making voice calls over the Internet by 1999 (1)
Internet telephony will account for 12.5 billion minutes of use by 2001 (2)
25% of all the world’s phone calls will travel on the Internet within 12 years (3)
By 2002, 18.5% of all domestic phone traffic will be carried over data lines (4)

## Slide 6: Current Market Initiatives
Internet Telephony eXchange Carrier (ITXC)
  Offers wholesale access to and settlement of IP-based telephone calls
  Uses iPass settlement technology
  Funded by AT&T and VocalTec
Qwest Communications International, Inc.
  Announced a 7-by-24, 7.5¢/minute telephone service
  Uses a brand-new, high-capacity, fiber-optic network using VoIP technology
AT&T WorldNet Services (AT&T Jens)
  AT&T @phone service for internet telephone calling within Japan and to international locations
  Announced a 7¢/minute IP-based telephone service

## Slide 7: Three Components for the IP Voice / Fax Product Offering
IP Multimedia Components
Store & Forward
FAX Server Support
Core Network Replacement
&
PC, Phone and FAX Support
Product &
Software
Features
Applications
Product Infrastructure for Data, Voice and Video
MAX/MAXTNT
Message
Interface
IP Voice
H.323
Standard
IP FAX
“Real Time”

## Slide 8: What is the MultiVoice Gateway for the MAX?
Voice and Fax Traffic
Frame Relay
MultiVoice
Gateway
Ethernet
Uses ITU-T H.323 to encode Voice into IP packets
Can output IP voice onto Ethernet or Frame Relay
Uses RFC1490 IP over Frame Relay
Works on the industry-proven and market-leading MAX Platform
NetMeeting
CoolTalk
PBX
MAX
Frame/ATM
Core Network
T1/E1 PSTN Interfaces
PSTN

## Slide 9: MultiVoice for the MAX - Configuration
Standard
Telephone
Fax
MultiVoice
Access Manager
(H.323 Gatekeeper)
NetMeeting
CoolTalk
PSTN #1
H.323 PC
Endpoint
Standard
Telephone
Local PSTN Network
Local PSTN Network
VoIP Network
MultiVoice
Gateway
MAX
Fax
Frame/ATM
Core Network
PSTN #2
MAX
PSTN #1
IP
IP

## Slide 10: MultiVoice Component Overview
MultiVoice Gateway for the MAX
  Terminates the native PSTN network interfaces (e.g. T1, PRI, E1 and BRI)
  Supports various voice compression codecs
  Support ITU-H.323 protocol for Phone-to-Phone and Phone-to-PC communications over the IP packet network
MultiVoice Access Manager (H.323 Gatekeeper)
  Manages the H.323 zone(s) for a set of gateways and PC endpoints
  Provides address translation (E.164 telephone address to IP address)
  Supports client registration (authentication)
PC Endpoints
  Any standard H.323-compliant PC software that supports voice calls (e.g. NetMeeting or CoolTalk)

## Slide 11: MultiVoice Fax - Configuration
Fax
MultiVoice
Access Manager
(H.323 Gatekeeper)
PSTN #1
Local PSTN Network
Local PSTN Network
VoIP Network
MultiVoice
Gateway
MAX
Fax
Frame/ATM
Core Network
PSTN #2
MAX
PSTN #1
IP
IP
Future RT Fax-capable
H.323 endpoints
Store & Forward
Fax Server
MultiVoice Fax
Store & Forward Fax
Real-Time Fax

## Slide 12: Why Fax over IP?
Use common infrastructure for data, voice, and fax
Fax is 40% of all PSTN traffic
Fax is better suited to transport over IP
Provide new services
  Fax broadcast
  Fax to e-mail conversion
Save big bucks

## Slide 13: Real-Time vs Store and Forward
Real-Time (RT) Fax over IP
  When it’s sent, it is REALLY sent!
  No storage in the network
  No looking for “lost e-mail/faxmail”
  Takes about the same amount of time as fax over PSTN
  Replaces existing fax service
Store & Forward (S&F) Fax over IP
  Faxes are stored on a server in a network
  Enables group broadcast of fax
  Enables new services, But, ... Like e-mail, there may be ...
    Lost faxes
    Delays of an unpredictable length
  Not suitable for critical documents, contracts, etc.

## Slide 14: General Characteristics of the Fax Gateway
Supports both S&F and Real-Time operation
Three models
  S&F only solution
  Combined S&F / RT Fax gateway (RT-A)
  Combined RT Fax / Voice gateway (RT-B)
Supports E1 and T1 signaling direct from MAX product
  R2,Robbed Bit, PRI etc.
Supports standards
  Will support finalized ITU-T T.ifax2 and IETF RFCs
  Will be available in pre-standard versions
RT solution shares infrastructure with Ascend MultiVoice Gateway
  Uses same Gatekeeper, CDR, etc. technology

## Slide 15: MultiVoice Access Manager
Standard
Telephone
Fax
MultiVoice
Access Manager
(H.323 Gatekeeper)
NetMeeting
CoolTalk
PSTN #1
H.323 PC
Endpoint
Standard
Telephone
Local PSTN Network
Local PSTN Network
VoIP Network
MultiVoice
Gateway
MAX
Fax
Frame/ATM
Core Network
PSTN #2
MAX
PSTN #1
IP
IP

## Slide 16: Importance of the … MultiVoice Access Manager
VoIP Vision – “The Packet Network is the future PSTN”
The Access Manager for the MAX plays an important role in this vision
  Future versions of the MultiVoice Access Manager will support advanced telephony services and applications
  These applications provide functions that allow ISPs to offer telco-like services in addition to value-added, integrated multimedia applications
  Tighter-integration with existing PSTN features, e.g. SS7 integration – important for PSTN / VoIP co-existence in carrier networks

## Slide 17: Scaling MultiVoice for MAX
Start with MAX 6000-based Gateway
  Supports 16 to 96 voice ports per MAX chassis
Access Manager is standard NT / SOLARIS based
  Cheap PC up to massive, duplicated server
  H.323 supports “backup” gatekeepers if primary fails to respond
  Support for multiple Access Managers in the same network
Endpoints find Access Manager via
  Fixed administration
  Multi-cast (LAN)
  DNS (Internet / H.323 V2)
Access Manager send calls to foreign Gateways via DNS
  Ascend value-add – use of common DNS server
  Simple provisioning

## Slide 18: MultiVoice for MAX - Accounting / Billing One System for Voice and Fax
RADIUS
Navis™
3rd-party Billing
CDR Records
MultiVoice
Access Manager
MultiVoice
MAX Gateway(s)

## Slide 19: MultiVoice Access Manager System Architecture
Access Manager
Application
HTTP
Server
Network
Interface
IP Network
CGI
GKCP/
HTTP
RAS
Registration,
Admissions, and
Status
User
Database
(local or remote)
Gateway
Database
(local or remote)
RADIUS Server
Access Manager Server
MultiVoice
Gateways
GKCP/
HTTP
RADIUS
H.225
ODBC
HTML
forms
announce-
ments
API
System
Manager

## Slide 20: Application: MultiVoice for MAX with B-STDX and Frame Relay
Packet Voice Access shelf for B-STDX 6K, 8K, 9K
Conforms to RFC1490 for switching by IP Navigator or generic Frame Relay
Support for Type-of-Service (ToS) bits for QoS
Frame Relay SVC Support
NetMeeting
CoolTalk
Frame Relay
MultiVoice
Gateway
Ethernet
B-STDX 9000
MAX
PBX
PSTN
Up to 4 T1/E1
Interface(s)
Ethernet

## Slide 21: Application: ISP Voice Bandwidth Provider
Use ISPs existing IP Network to transport voice
Packet voice access for B-STDX core switch
IP Navigator QoS guarantees delivery and quality
Offers new ISP Revenue opportunities
Company A
Company B
Company C
MultiVoice
Gateway
B-STDX
MAX
B-STDX
MAX
Frame
Relay
MAX
MultiVoice
Gateway
MultiVoice
Gateway
Company A
Company B
Company C
Notes: Page <number>
<footer>
<header>
<date/time>
14

## Slide 22: Absolute QoS : Toll-Quality Voice over IP
MultiVoice
Gateway
IP Navigator Network Set-up Circuit Guaranteeing Toll-Quality
CBX 500
BSTDX 9000
IP WAN QoS Capabilities via IP Navigator
  Best effort service
  Relative type of service (ToS) in IP header
  Absolute QoS using “on demand” guaranteed bandwidth
MultiVoice
Gateway
MultiVoice
Gateway
MultiVoice
Gateway
PSTN
PSTN
PSTN
PSTN
PSTN
PSTN
PSTN
MultiVoice Gateway
voice to IP gateway

## Slide 23
MultiVoice for MAX
Release 1.0
Product Specifics

## Slide 24: MultiVoice for MAX Release 1.0 Key Features
MultiVoice Gateway for the MAX - Release 1.0
  Phone-to-Phone H.323 operations – standard gateway operation
  Telephony WAN interfaces – support for T1, T1/PRI, E1, E1/PRI, BRI
  Packet network interfaces – Ethernet and Frame Relay
  Voice codec support – support for G.711 and G.729(A)
  Voice VPN support – for enterprise deployment that do not required user authentication
  Hybrid-line echo cancellation – remove echo created by 4/2-pair network interfaces
  DTMF detection and generation – emulation of PSTN capabilities

## Slide 25: MultiVoice for MAX Release 1.0 Key Features
MultiVoice Access Manager Release 1.0
  ITU-T H.323-compliant Gatekeeper implementation – support for RAS protocol
  Phone-to-IP address translation – call routing within the IP network
  Web-based administration interface – remote administration via a standard browser
  PIN-based user authentication – user authentication for network access
  Voice VPN support – for enterprise deployment that do not required user authentication
  Telephone number aliases – support for private numbering plans

## Slide 26: MultiVoice for MAX Release 1.0 Key Features
MultiVoice Access Manager Release 1.0
  Call Accounting Records (CDR) – detailed call record for billing system integration
  Gateway and user database support – flat file or ODBC database integration
  Third-party billing system support – interfaces for supporting third-party billing applications
  Microsoft Windows NT v4.0 support – Access Manager runs as a NT application

## Slide 27: MultiVoice for MAX Release 1.0 Gateway H.323 Implementation
Audio Codec
G.711, G.729(A)
H.225.0
(RTP)
System
Control
H.245 Control
H.225.0
RAS Access
Manager Int.
Q.931 Call
Setup
Multi
Voice
Voice-
over-IP
Network
Interface
(LAN/FR)

## Slide 28: MultiVoice for MAX Release 1.0 Configurations
MAX 6000-based Bundles
  48-port T1 System
  96-port T1 System
  60-port E1 System
  90-port E1 System
MAX 6000-based QuickStart Bundle
  16-port T1 System
  16-port E1 System
  16-port E1/BRI System
MAX 400x-based Upgrade
  MAX 400x T1 SW Upgrade
  MAX 400x E1 SW Upgrade
MultiVoice DSP Slot Cards
  DSP16
  DSP12
  DSP8
MultiVoice Access Manager
  4 GW System
  32 GW System
  128 GW System

## Slide 29: Application: Basic Voice Services
Single Network Design
  Use of a single data network to provide both data and voice based services
Billing that scales with network usage
  Per minute billing (e.g. ¢/min) for long distance voice services
New network service revenues for non-traditional services
Hong Kong
Tokyo
New York
MultiVoice Access
Manager
Network Service Provider
MultiVoice
Gateway
MAX Remote
Access
MultiVoice
Gateway
MultiVoice
Gateway
IP-over-Frame Relay
Local
PSTN
Local
PSTN
Local
PSTN

## Slide 30: Application: Local 800 Services
Lower operational costs
Use existing ISP Point-of-Presence (POP) to provide a voice network for customer support
End-user dials a local number for access to customer support agents
Calls are routed to ACD via the existing data network in order to reduce long distance 800 service costs
MultiVoice Access Manager (MVAM)
MultiVoice GW
MultiVoice GW
ACD Agents
Local “800 Service”
Traditional “800 Service”
Los Angeles
San Francisco
PBX
IXC
Local
PSTN
IXC
IP NET
ACD

## Slide 31: Application: PBX Trunk Extension
Enterprise private networking
Point-to-Point PBX trunk replacement
Use QoS capabilities to insure toll quality voice calls
PBX
4 T1/E1
PBX
Hong Kong
New York
MultiVoice
Gateway
MultiVoice
Gateway
4 T1/E1

## Slide 32: Application: PBX Trunk Intraflow
Alternate route for voice calls across packet data network
Automatic intraflow for PSTN (Dial 9 access)
Operational cost savings
Hong Kong
Tokyo
New York
MultiVoice
Access Manager
Dial 8
Dial 9
MultiVoice
Gateway
MultiVoice
Gateway
MultiVoice
Gateway
Local
PSNT

## Slide 33: MultiVoice for the MAX – Advantages for Different Markets
Advantages to ISPs
  New service offering and revenue from existing customer base
  Obtain a higher return on existing network by using existing infrastructure
  Cost justify increased internet access capacity (higher speed Pipeline® for SOHO locations)
  Transaction-based billing which scales with network usage
Advantages to Telcos
  Backbone provider revenues
  Revenues from leased lines
  Revenues from local calls (call completion – phone doubler-application)
  Two-tier pricing system (circuit-switched services / packet-switched services)

## Slide 34: MultiVoice for the MAX – Advantages for Different Markets
Enterprise
  Use spare capacity in internal packet network (Intranet) to carry voice between PBXs in private networks (Intraflow)
  Backup for existing voice truck (Tie-lines)
  Support small or branch office locations over a single packet network
  Can deploy MAX on the premise (Local gateway)