## Slide 1
Traffic Management
Traffic Management Service Categories
QoS
Call Admission Control (CAC)
Traffic Policing
Congestion Management
Packet Sub-System
Cell Sub-System

## Slide 2: Traffic Management
Support multiple Service Categories for packet and cells
Service Categories
  Constant Bit Rate (CBR)
  Real Time Variable Bit Rate (rt-VBR)
  Non Real Time Variable Bit Rate (nrt-VBR)
  Unspecified Bit Rate (UBR)
  Available Bit Rate (ABR)
ATM Forum TM 4.0 compliant architecture

## Slide 3: Traffic Parameters
Traffic Parameters
  Peak Cell Rate (PCR)
  Sustainable Cell Rate (SCR)
  Maximum Burst Size (MBS)
  Minimum Cell Rate (MCR)
  Feedback (RM Cells)

## Slide 4: TM 4.0 Service Definitions

## Slide 5: Quality of Service (QoS)
QoS provides ability to offer services which guarantee advertised QoS Parameters (CTD, CDV, CLR)
CAC guarantees resources are available for QoS Guarantee
CAC reserves resources when connection established
Overbooking of Cell Buffers and Bandwidth is allowed
If Overbooking is used QoS is not guaranteed

## Slide 6: Connection Admission Control (CAC)
Accepts connections based on availability of node resources
  Bandwidth, Buffer, VPI / VCI
Checks that source and destination are reachable
Checks for valid traffic descriptors
Can configure for overbooking of bandwidth and cell buffers
Enable / Disable bandwidth CAC on a per port basis

## Slide 7: CAC Connection Management
Hardware
Drivers
Call Buffer
Resources
PNNI
Smart PVC
Manager
Port Bandwidth
Resources
POD
APP
MIB
CPOD
Cell Highway
Bandwidth
Resources
Network
Routes
SVC
Manager

## Slide 8: CAC Connection Processing
CAC
Cell Buffers
(Oversubscription)
Bandwidth
(Oversubscription)
VPI / VCI Range
VP / VC Available
Port Good
Traffic Descriptors
IPOD
XPOD
IPOD
Port
XPOD
Port
Cell
Highway

## Slide 9: Configurable CAC Parameters
Enable / Disable bandwidth CAC
Size of variable bandwidth pool
Percentage of variable bandwidth applied against fixed bandwidth pool
Bandwidth and buffer overbooking percentage per service class
Input & Output cell buffer distribution
VPI / VCI ranges
File based configuration (Release 1.0)

## Slide 10: Service Categories QoS Bandwidth Allocations

## Slide 11: “Traffic Policing” Usage Parameter Control (UPC)
Ascend’s Broadband Access products employ a UPC function that is designed to:
  Discard cells with invalid, or unprovisioned VPI / VCIs
  Monitor traffic rate to determine if it conforms to the traffic parameters
  Tag (to CLP=1), discard or pass non-conforming cells
Enhanced PODs only

## Slide 12: Dual Generic Cell Rate Algorithms (GCRA’s)
L + I
“I” added
for each cell arrival
1 Unit leaks per unit of time
(e.g drains at PCR or SCR)
“I” Affects cell Rate
“L” Affects cell bursts
GCRA employed on a per connection basis
Dual Leaky Bucket Algorithm program based on Traffic Parameters and CDV
First Bucket - PCR 0+1
Second Bucket - SCR 0 or SCR 0+1
GCRA (I, L)
  PCR I= 1/PCR, L = CDV
  SCR I= 1/SCR, L = BT + CDV where BT= (MBS-)(Ts-T)
ATM Forum UNI 3.0, 3.1, TM 4.0 and ITU I.371

## Slide 13: Congestion Management
Congestion control is concerned with logically controlling congestion when it occurs:
  Per channel, per priority, and per cell highway congestion limits are configurable
  Per channel choice of the following congestion management strategies:
    Cell Loss Priority (CLP) marked cell dropping
    Explicit Forward Congestion Indication (EFCI) cell marking
    ATM AAL5 Early Packet Discard (EPD) & Partial Packet Discard (PPD)
  Traffic shaping for packet based traffic (1/PCR)
  Backpressure - Output to input queue congestion notification

## Slide 14: VPI / VCI Ranges
Can be configured on a per POD basis
PVPs require a reserved VP range (per port)
Configure via file
Defaults:

## Slide 15: Packet Subsystem
Provides ABR (RM, Rate Packets) support in accordance with TM 4.0
Provides per VC queuing and traffic shaping
Supports 32 ABR rate packs (Traffic Profiles)
SIMM based buffer system
Traffic Shaping
  Continuous rate shaping (1/PCR)
  Transmit schedule
  VBR support

## Slide 16: Packet Buffering
ICM
SERIAL
PORT 1 & 2
INTERFACE POD 1
INTERFACE POD 2
Packet Bus
Cell Bus
PROTOCOL
ACCELERATOR™
Incoming Packets
Per VC Queues
Outgoing Cells
XPOD
CAM
(2000 MAC)
Incoming Packets
RM Cell
CBR
Multicast
VBR
UBR
ABR
10%
1%
89%
Receive RM
Cell Processor
RM Cell
Generator
CELL POD
Header
Mask
Transmit
Scheduler
Receive
Processor
SIMM
Packet
Buffers
4 Mbytes
(Standard)
5400
8 Mbytes
10,800
MANAGEMENT PROCESSOR

## Slide 17: Cell Buffering
Advanced integrated modular buffer architecture
  Provides buffering at input and output controllers as well as switching (CPOD)
  Per channel and per-priority maximum queue lengths are configurable
  Per priority oversubscription is configurable
  Per channel, per-priority and per-device congestion limits are configurable
  “Back-pressure” flow control mechanism provides efficient usage of all buffering resources

## Slide 18: Cell Buffering
ICM
SERIAL
PORT 1 & 2
PROTOCOL
ACCELERATOR™
MANAGEMENT PROCESSOR
INTERFACE POD 1
INTERFACE POD 2
XPOD
Packet Bus
Cell Bus
CELL POD
Per VC
Accounting
&
Congestion
Management
CBR
Multicast
VBR rt
UBR / ABR
OAM
VBR nrt
10%
1%
14%
25%
50%
Per VC
Accounting
&
Congestion
Management
CBR
Multicast
VBR - rt
UBR / ABR
OAM
VBR - nrt
10%
1%
14%
25%
50%
Up to 6,000 Cells Input Buffering
Per VC Accounting and Congestion Management
Buffer distribution is User Configurable (shown above are default settings)
Traffic Policing **
** Enhanced Version
Up to 4,000 Cells Output Buffering **
Back Pressure to Input Stage on Congestion
Feedback
Incoming Cells
Outgoing Cells
CBR
Multicast
VBR
UBR
ABR
10%
1%
89%

## Slide 19
Thank You
Part #