## Slide 1
MAX 6000
WAN Access Switch
Dana Harrison
Director, MAX Product Mgmt

## Slide 2: MAX 6000 Product Presentation Table of Contents
MAX 6000 Overview
MAX 6000 Advantages
  Performance
  Expandability
  Reliability
Slot Card Support
Digital WAN Access
True Access™ Operating System (TAOS) 6.0
  Intragy™ for the Enterprise
  Virtual Private Networking
  Security
  Extensive Management Capability
Applications
Protocols Supported
Notes: The MAX 6000 is the next generation of 4T1/E1 WAN access switch technology and a landmark product for Ascend. It is designed from the ground up to meet the demands of our largest ISP’s, carriers, and corporate customers. The MAX 6000 is faster, has more features, and is more expandable than anything in its class, including the Cisco AS 5300, Lucent PortMaster 3, Shiva LAN Rover Access Switch, and Compaq 6100. In fact the MAX 6000 competes favorably with access switches costing much more including the 3Com Total Control and the Bay Networks 5000 MSX concentrator. We should be able to take market share from these competitors with the MAX 6000.
In this presentation we will look at the MAX 6000 hardware and software features, and see how the MAX wins against its competition.

## Slide 3: MAX 6000 Product Overview
Next Generation of MAX 4 T1/E1 Product Family
  Uses proven MAX software (True Access Operating System [TAOS] 6.0)
  Uses MAX multi-processor slot cards
Enhances Proven MAX Architecture
  Industry Leading Performance
  Most Comprehensive Range of Services (TAOS)
  Designed for Reliability and Serviceability
  Expandable DRAM, Flash Memory & Slot Cards
  Software Upgradable protocols and services
  Robust Power and Thermal Capacities
Notes: The MAX 6000 is a brand new hardware design. The only aspect of the MAX 6000 that was defined up front was compatibility with Ascend’s True Access Operating System (TAOS), and with the existing MAX Slot Cards. The design goals were to achieve best in class performance for modem and digital calls, increase power supply capacity and heat dissipation capacity to meet the most rigorous reliability standards (NEBS Level 3), and provide practically limitless expandability in DRAM, Flash memory, slot cards, and MAX Stack. All of these hardware goals were met.
The area where the MAX 6000 enjoys its biggest advantage is in its comprehensive list of WAN access features. TAOS 6.0 has added 132 new features (see slide 16 for more detail) to put the MAX farther ahead of the competition. TAOS 6.0 is also the product of new software development process that significantly increases the amount of regression testing to enhance system reliability.

## Slide 4: MAX 6000 Hardware Interfaces
4 T1/E1/PRI
Autosensing 10/100Base-T RJ-45
V.35 serial (up to 8 Mbps)
RS-232 console port
Memory slots
  Custom DRAM (up to 32MB)
  PCMCIA FLASH (up to 8MB)
6 slots for MAX slot cards
Available in AC or DC
Console
10/100 Connection to LAN
Alarm Relay
V.35 Serial
PCMCIA slot
for FLASH
Custom slot
for DRAM
T1/E1/PRI to
WAN or PBX

## Slide 5: MAX 6000 Enhanced Performance and Expandability
Enhanced System Performance
  Central processor – latest in Intel i960 processors
  Multiprocessor architecture with Series56™ Digital Modems
  High-port density
    Up to 96 Series56 Digital Modems
    Up to 120 digital connections (ISDN, Frame Relay)
  Support for Fast Ethernet (autosensing 10/100BASE-T)
  Enhanced hardware compression capability
Enhanced Memory Expandability
  2 MB of FLASH, expandable to 10 MB via PCMCIA slot
  16 MB of DRAM, expandable to 48 MB via custom slot
Enhanced Heat Dissipation and Power Capacity
  Improved thermal design increases airflow, lowers temperature
  Increased capacity power supply
Notes: Another important design advantage of the MAX 6000 is its expandability. 16 MB of shared DRAM now comes standard on the system board versus 8 MB with the and can be expanded to 24MB or even 32 MB in the future. The 6000’s also supports an optional private DRAM pool for the CPU that can be used to run system code and tables without contending for the shared I/O bus at all. The MAX software load and configurations are kept in Flash Memory, and the MAX 6000 has much more room than its predecessor. The on-board Flash continues to provide 2 MB, but this can be easily augmented with the addition of an 8 MB Flash PC Card.
In addition to data throughput performance improvements, the MAX 6000 is designed to the highest standards in mechanical, electrical, and thermal tolerance, capacity, and safety. Components were selected for

## Slide 6: MAX 400X / 6000 HW Comparison
25 MHz i960CF
8 MB Shared DRAM
No private i960 DRAM
2 MB Flash Memory
1 STAC 9706 compression processor
No DMA
10 BASE-T Half Duplex + AUI
Hardware Pins
64 HDLC Channels
64 MHz i960HD
16 to 32 MB Shared DRAM
32 MB Private DRAM
2 + 8 MB Flash Memory
2 HiFn 9711 compression processors
4 channel DMA controller
10/100 BT Full Duplex, Autosensing, No AUI
Software controlled settings
128 HDLC Channels
MAX 400X
MAX 6000

## Slide 7: MAX 6000 vs Competitors Modem Performance
Source: The Tolly Group, Preliminary, Feb 1998
Note: Cisco AS 5300 does not yet support 56K modem speeds

## Slide 8: MAX 6000 vs Competitors ISDN Performance
Source: The Tolly Group, Preliminary, Feb 1998
Source: The Tolly Group, Preliminary, Feb 1998

## Slide 9: MAX 6000 Hardware Designed for Reliability & Serviceability
100% NEBS Level-3 compliant design
200% power supply capacity of the MAX 400X
Dramatically improved airflow with separate air channel for power supply.
Hot Fail-over Flash boot image
External Flash to internal Flash software download
Components and packages chosen to improve mechanical and thermal durability and reliability
Enclosure can be opened easily without special tools.
Notes: The MAX 6000 was designed to operate reliably in the most demanding thermal, mechanical, and electrical environments. Many of its subsystems were over-designed to accommodate future expansion with headroom to spare. The MAX 6000 is easily field servicable without special tools or expertise.
The environmental conditions in which the 6000 is designed to operate are validated in Level 3 of the Network Equipment Building Standard certification test process. During NEBS testing, the equipment is subjected to extremes of temperature, humidity, vibration, mechanical impact, electrical shock and component failure. Here, the MAX 6000 is up to the test. With larger more efficient fans, an air flow optimized component layout including a separate air flow chamber for the power supply, a power supply with over 50% headroom beyond the maximum power configuration, a rigid chassis to avoid mechanical stress on electronic components, and electrical isolation on key subsystems, the MAX 6000 defines the industrial strength WAN Access Switch.
Other measures that were taken to design reliability into the MAX 6000 include full system simulation of boundary conditions, a hot fail-over system boot image in Flash with the ability to test run a software load before making it permanent, and In Circuit Testing on every unit to locate and correct even small deviations well within specification, but not up to the rigorous standards of the MAX 6000.

## Slide 10: MAX 6000 Software Reliability New Software Development Process

## Slide 11: MAX 6000 Memory Expandability
Shared DRAM (i960, HiFn’s, Ethernet, SCA)
  16 MB on internal daughter board (standard)
  Future expansion possible to 24 and 32 MB
Private DRAM (bus for i960 only)
  32 MB available on proprietary external DRAM card (optional)
  Future expansion possible to 128 MB
Flash Memory
  2 MB on system board
  8 MB Flash expansion with optional PC Card
  10 MB total Flash memory
Notes: One of the key advantages of the MAX 6000 is its expandability.

## Slide 12: MAX 6000 Line Expandability Available slot cards
Series56 Digital Modems
  Available in 8-, 12- or 16-port densities
  Mixed densities allowed
V.34 Digital Modems (Available with True Access Operating System [TAOS] 6.0.1)
  Available in 8- or 12-port densities
IDSL
BRI (Network Services or Terminal)
IMUX (available with TAOS 6.0.1)
  2-port IMUX cards for videoconferencing/backup & overflow
  6-port IMUX cards for videoconferencing
V.110 (GSM)
Personal Handy-Phone System (Japan PHS)

## Slide 13: MAX 6000 Series56 Digital Modem Cards
Digital Modems with Rockwell K56flex Technology
High-performance DSP-based Hierarchical Processing
  Provides multiprocessor architecture
Simultaneous 33.6 Kbps and 56 Kbps Access Speeds
  V.42 Error Correction and V.42bis Compression
  MNP10 EC for cellular data calls
Software Upgradable for Long-Term Hardware Viability
  Software Upgrade to the ITU 56K modem standard (V.90)
  Series56 hardware investment protection
8-, 12-, 16-port Series56 Modem Cards can be mixed
Notes: Ascend pioneered digital modem technology and takes it to the next level in the MAX 6000. From 8 to 96 Series 56 digital modems can be configured simply by plugging MAX Slot Cards into the six slots in the MAX 6000. Each group of 4 modems has its own co-processor to provide non-blocking performance. Because the modem modulation is implemented in firmware on a powerful Rockwell DSP, all Ascend Series56 cards are software upgradable to the ITU V.90 56K modem standard. Also, because Ascend uses the same code that is licensed and tested by so many other manufacturers, MAX modem reliability and interoperability are best in class.

## Slide 14: Other MAX 6000 Improvements
External PC Card Slots for adding Flash and DRAM
PRI to T1 Conversion available on all ports
Faster MAX Stack with 100BASE-T Ethernet

## Slide 15: MAX 400X / 6000 Product Positioning - Performance, Performance, Performance
The Best Performing Remote Access Server 2U High for General Internet POP deployment, IDSL service delivery and Enterprise Access
MAX 4030/4060 for entry-level ISP and Corporate access deployment
MAX 6000 for high performance ISP and corporate access deployment

## Slide 16: MAX 6000 System Software Kernel, Extensions, and Applications True Access Operating Systems (TAOS) 6.0
IntragyCentral™
Global Digital
Access
Tunneling
Secure Access
Firewall
NavisAccess
Option
Inverse MUXing
Virtual
Routing
Future
Extensions
NavisAccess™
IntragyAccess™
Ascend Access Control™
IP
Router
AAA
Server
Bandwidth
Manager
Terminal
Server
WAN Access
Server
Management
Agent
Modem
Manager
Scalability
Agent
DSP
Manager
TAOS Extensions
TAOS Kernel

## Slide 17: True Access Operating System (TAOS) 132 New Features
9 new Hardware features
10 new Line Interface features
27 new WAN Access features
6 new IP Routing features
4 new OSPF Routing features
2 new Multicast Forwarding features
4 new IPX routing features
9 new AppleTalk routing features
25 new Authentication and Accounting features
19 new Administrative features
17 new SNMP features
Note: Please see TAOS 6.0 Release Notes for descriptions of each of these features.

## Slide 18: True Access Operating System TAOS 6.0
Enterprise Functionality
  Intragy
Virtual Private Networking
Security Options
  Secure Access Firewall
  RADIUS and Ascend Access Control
Software Options
  Global Digital Access™ 6000
  MAX Stack
Extensive Management Capability
  NavisAccess
  Java-Based Ascend Configurator

## Slide 19: Software Bundles Intragy
Intragy
  Software solution for corporate multiprotocol environments
  IntragyCentral
    Transparent Bridging
    Multiprotocol Routing
      Adds IPX and AppleTalk routing
    Multiprotocol Access
      Adds IPX and AppleTalk Remote Access
    DeskDial
  Client Dial Software
    IntragyAccess

## Slide 20: MAX 6000 IntragyCentral with IntragyAccess
Corporate LAN
Mobile User
Seamless access to network resources from remote location
Award-winning complement of software included
MAX 6000 with IntragyCentral
Analog
ISDN BRI
Pipeline 75
Remote User
Analog
Modem
Modem
T1/E1/PRI
Home User
Laptop with
IntragyAccess
PC with
IntragyAccess
Carrier
Services

## Slide 21: MAX 6000 Intragy - DeskDial
Corporate Headquarters
T1/E1/PRI
ISDN BRI
Telecommuter
LAN-based Data / Class-3 FAX Out-Dial
Multiprotocol Support
DOS, Win 3.X, Win95 Support
Easy Installation and Maintenance
Call Activity Audit Capability
FAX
MAX 6000
Dial/FAX
Out
Pipeline 75
Analog
T1/E1/PRI
PSTN
Online
Services
Internet

## Slide 22: MAX 6000 Virtual Private Networking
Ascend Tunneling Management Protocol (ATMP)
  GRE tunneling
  Mobile-IP
  IPX protocol spoofing
Frame Relay Direct
Point-to-Point Tunneling Protocol (PPTP)
Layer-2 Tunneling Protocol (L2TP)
Raw TCP tunneling
IP Direct
Extended RADIUS authentication and profile management

## Slide 23: MAX 6000 Virtual Private Networking
Carrier
Services
Modem
Access Control
T1/E1/FT1
ISDN BRI
backup
ISDN BRI
Analog
T1/E1/PRI
Pipeline 130
Pipeline 50
Corporation #1 Central Site
MAX 6000 with Secure Access Firewall
ISP POP
Corporation #1 User
Corporation #2
Telecommuter
LAN
LAN
T1 Frame Relay
Corporation #2 Central Site
PC
MAX 6000 with Secure Access Firewall
MAX 6000 with Secure Access Firewall
T1/E1/FT1
Corporation #2 User

## Slide 24: MAX 6000 Security
Secure Access Firewall
  Dynamic ICSA-certified “stateful inspection” firewall
  Explicit permit and deny
  Rules adapt to type of traffic
    Network address, host names, UDP, TCP, ICMP, source/destination ports, send/receive direction, TCP session state, time, application port number, etc.
  Eliminates need for proxy application gateway
  Secure Access Manager (configuration utility)
  Comprehensive audit trails for tracking
RADIUS and Ascend Access Control (extended RADIUS)

## Slide 25: MAX 6000 Security Options - Corporate Internet Gateway
Mobile User
Single secure high-speed connection to Internet
Token card authentication and Secure Access Firewall and Extended RADIUS Capabilities
Ascend Access
Control
(extended RADIUS)
ISDN
PRI
Leased Line or
Frame Relay
ISDN BRI
ISDN BRI
Analog
56 Kbps
Ethernet
Frame Relay
or V.35
IntragyAccess
with Token card
Regional Office
MAX 6000 with
Secure Access Firewall
MAX 2012/24 with
Secure Access Firewall
Corporate Network
Pipeline 75 with
Secure Access Firewall
Home Office
Carrier
Services
Internet

## Slide 26: Global Digital Access 6000
Software solution allows variety of access connectivity
Digital Access
  56/64 Kbps B-channels for ISDN
  56/64 Kbps Frame Relay
  Up to 120 remote sessions
ISDN PRI signaling
  Enables PRI signaling for T1/E1 ports
Frame Relay support
  Up to 4096 PVCs with RADIUS authentication

## Slide 27: MAX 6000 High Performance MAX Stack
Carrier
Services
T1/E1/PRI
T1/E1/PRI
T1/E1/PRI
ISDN
MAX 6000
ISDN Terminal Adapter
B2
B1
Application Server
Central Site
Remote Site
Multiple MAX system operating as single logical unit
Shared-resource operation
  Shared IP pools
  MP, MP+ and BACP calls span stack
  Single virtual Network Access Switch
  Scalable architecture using software
Higher MAX Stack performance over 100BASE-T

## Slide 28: Ascend Management Extensive Management Capabilities
Java-Based Ascend Configurator
  Installation and configuration utility
NavisAccess
  Discovery and Mapping
  Element Management
  Summary View
  Configuration Management
  Fault Management
  Performance Management
  Capacity Planning
  Security and Accounting

## Slide 29: NavisAccess Discovery and Mapping
Utilizes HPOV discovery and mapping
Augments HPOV with multi-layer hierarchical map
  Network Layer: IP
  Link Layer: Frame Relay, ISDN
  Physical Layer: DS1, E1, PRI, BRI, xDSL
Application access via map
Remote Office 1
Remote Office 2
3COM
507_1
CISCO
Kellum
PIPELINE
204.220.20.4
LAN 1
West Coast MegaPOP
East Coast POP
European HQ
204.220.20.4
GRF
isigw
Network Backbone
CISCO
Sunburn.netstar.com
PIPELINE
buzz.netstar.com
MAX TNT
kiev.netstar.com
Midwest POP
222.221.21.0
200.200.90
MAX TNT
denver.netstar
ISDN
FR
ISDN
FR
PIPELINE
torpedo.netstar.com
Carrier
204.220.20.4
206.117.324
Corporate Central
Cisco
Tonga

## Slide 30: MAX 6000 Target Applications
Fully-featured WAN Access Switches for:
  Carrier and Internet Service Provider POPs
  Corporate remote and Internet access
Ideal Platform for ISPs and Carriers
  Low entry price with high-end feature set
  Easy set-up using Java-Based Ascend Configurator
  Extensive network design flexibility as network grows
  Extensive POP management with multi-vendor support
Well-suited for Corporate and Business Applications
  Multiprotocol access and multiprotocol routing support
  Extensive access functionality / flexibility
  Network management with performance analysis tools

## Slide 31: MAX 6000 Application ISP POP Concentration
Pipeline 25-Px
Provide dialed and leased services
Concentration of local POPs
Routed
Backbone
Dial-up Services
Dial-up Services
Remote Office
Analog
(56 Kbps)
T1
ISDN BRI
ISDN
PRI
Local POP
ISDN
BRI
T1/
Frame
Relay
MAX 6000
Pipeline 50
Pipeline 130
MAX 6000
K56flex-
compatible modem
Mobile User/
Home User
Home User
ISDN
PRI
ISDN
BRI
Pipeline 75
T1/E1
High-density session terminations
Redundant networking
ISP POP
ISDN BRI
Backup
GRF
Fast Ethernet
Carrier
Services
Carrier
Services

## Slide 32: MAX 6000 Application ISP Remote POP
Internet
Maximum density up to 96 (T1) or 120 (E1) concurrent sessions
Provide dialed and leased services
Analog and digital sessions
K56flex / V.34 modems, ISDN and Frame Relay
Remote POP
To ISP Backbone Router or Switch
T1/
Frame
Relay
Mobile User/Home User
Modem
ISDN BRI
Backup
Analog
Remote Office
Pipeline 130
T1/E1/PRI
T1/Frame Relay
MAX 6000
ISDN
BRI
Telecommuter
Pipeline 75
Carrier
Services

## Slide 33: MAX 6000 Application Corporate Remote Access
Regional Office
Remote User
Branch Office
Corporate Central Site
MAX 2000
T1/E1/PR1
FT1/Frame Relay
FT1
MAX 6000
Pipeline 130
Pipeline 50
ISDN
BRI
ISDN BRI
Backup
Up to 96 modems
Up to 120 digital sessions
Integrated authentication
Multiprotocol access
Carrier
Services

## Slide 34: MAX 6000 Application Frame Relay Backhaul via V.35 Interface
8 Mbps Serial WAN Interface
Mobile/Home User
Remote Office
Analog
ISDN
BRI
T1/
Frame
Relay
MAX 6000
Pipeline 130
V.35 8 Mbps
Serial WAN interface
T1/E1
Modem
ISDN BRI
Backup
Home User
Pipeline 75
Regional POP
Router
T3
T3
Local POP
MAX TNT
Carrier
Services
Carrier
Services

## Slide 35: MAX 6000 Application Frame Relay Switching
High-speed WAN interface
UNI and NNI standard
Analog
Frame
Relay
ISDN BRI
T1/E1
PRI
MAX 6000
V.35 8 Mbps
Serial WAN Interface
Frame Relay
Switch
To FR
Backbone
ISDN BRI
Backup
Internet POP
Mobile User
Regional Office
Pipeline 130
Telecommuter
Pipeline 75
Modem
Laptop with
IntragyAccess
Carrier
Services

## Slide 36: MAX 6000 Application Videoconferencing
T1, E1, PRI,
BRI, SW56,
DDS56
Videoconferencing
MAX 6000
BRI to
Desktop
Workstations
ISDN
BRI
Central Site
Remote Site
Videoconferencing
ISDN
BRI
Carrier
Services

## Slide 37: MAX 6000 Application Backup and Overflow
Remote Office
Headquarters
MAX 6000
MAX 6000
T1/PRI
T1/PRI
Corporate backbone
Switch Circuits
Leased Circuit

## Slide 38: MAX 6000 Protocol Support
Routed LAN protocols
  TCP/IP via RIP, RIP2, OSPF
  AppleTalk and IPX (optional with Intragy)
Bridged LAN Protocols
  All (optional with Intragy)
WAN Protocols
  PPP, SLIP, C-SLIP, Async PPP, Sync PPP, X.25 PAD, X.25 over B-channel, V.110, V.120, D4 framing (T1/E1), G703/732 framing (R1), Frame Relay PVC, PPP-FR gateway, Frame Relay NNI, ISDN signaling (with Global Digital Access 6000), ARA (optional with Intragy)
Modem support
  K56flex, V.34, MNP 10-EC, MNP, V.42bis, fax modem dial out to 14.4 Kbps

## Slide 39: MAX 6000 Protocol Support (continued)
Bandwidth management
  Multilink PPP (MP), Multilink Protocol Plus™ (MP+), Bandwidth Allocation Control Protocol (BACP), TCP header compression, data compression (Ascend/Microsoft/STAC V9)
Security
  RADIUS, Ascend Access Control (optional), Secure Access Firewall (optional), TACACS, TACACS+, Password Authentication Protocol (PAP), Challenge Authentication Protocol (CHAP), token card, Calling Line ID (CLID), packet filtering, SNMP, console management (VT-100), PPP callback, user authentication
Virtual Private Networking (Optional)
  Ascend Tunneling Management Protocol (ATMP), Point-to-Point Tunneling Protocol (PPTP), Layer-2 Tunneling Protocol (L2TP)

## Slide 40: MAX 6000 Protocol Support (continued)
Intragy (Optional)
  Transparent Bridging
  Multiprotocol Routing: Adds routing support for IPX and AppleTalk
  Multiprotocol Access: Async IPX with local spoofing, AppleTalk Remote Access 1.0 & 2.0
  DeskDial
  IntragyAccess
Management
  NavisAccess, Java-Based Ascend Configurator, Telnet, NASI, SNMP MIB-2, PPP LQM, Frame Relay Annex D, Frame Relay ITU Annex A, Frame Relay ANSI Annex D

## Slide 41: MAX 6000 Product Structure

## Slide 42: MAX 6000 Product Structure (continued)

## Slide 43: MAX 6000 Product Structure (continued)

## Slide 44: MAX 6000 Product Structure (continued)

## Slide 45: MAX 6000 Product Summary
Enhanced Performance with New Architecture
  Faster processing
  Expandable memory
Supports MAX Slot Cards and Software
  Same configuration and management as MAX products
  Increased density of modem support
Robust Software Functionality
  Virtual Private Networking
  Multiprotocol support
  Extensive connectivity
Integrated Security
Comprehensive Management

## Slide 46: http://www.ascend.com